1:24 to 4:20 - repositioning tractor in manual mode
4:50 – network issues
15:39 – 16:40 – ramping up Kp to 74 to get movement on linear.x .3
17:55 – ctrl C to stop cmd_vel
18:15 to 18:47 - repositioning tractor in manual mode
20:15 to 20:30 – linear.x .5 Kp at 74 – ramps up and down; reduced Kp
27:03 to 27:30 - linear.x .75 Kp 45 – hovers around .4 m/s
27:45 to 28:30 - repositioning tractor in manual mode
36:40 to 37:17 - Trying 1.0 – varied between .6 and .8
37:26 to 39:00 – repositioning tractor in manual mode
42:40 to 42:59 – Running at 1.5 with Kp ~45 – looks like top speed was 1.1
43:12 to 44:53 - repositioning tractor in manual mode

Issues:
- target speed not achieved with Kp 45
- wifi was unstable
- .5 m/s was jerky at the beginning
- need to check actual speed
- GPS antenna needs remounting
- need odom_rtk and odom_wheel and ability to switch back and forth

What additional tests should be done?
- try different Kp settings – if you get it from params you can adjust remotely