Lawn Tractor Startup Procedures - 2024

Pre-Work
- Build path
- Copy {file} to {input_path.txt} Example - $ cp -i /home/tractor/ros1_lawn_tractor_ws/project_notes/paths/collins_62_step2.txt.txt /home/tractor/ros1_lawn_tractor_ws/project_notes/paths/input_path.txt

At Base Station
Make sure it has power, the GPS is receiving satellite signals and the radio transmit light is blinking.
At the Radio Control Unit
- Turn the unit on then turn on external power pack; Connect external power pack and ensure battery power is sufficient – Unsafe at 1900
- Put the mode switch to the bottom (pause mode); Put the throttle at Neutral; Move the steering to straight.

At the tractor
- Disengage transmission - pull lever at back
- Use BMS Software and check battery power
            - Note starting voltage ___________; If the battery voltage >= 13.2 volts you should be able to start the tractor
            - Engage Charge and Discharge functions in the app
            - Press RESET to monitor max discharge amps
- Make sure blade deck is UP
- Check gasoline level
- Ensure wiring connections are complete (Steer potentiometer, Steer motor, Transmission)
- Connect 12 volt supply to USB hub
- Make sure all other USB ports are on
- Turn on master power – GPS leds should light up
- Reset the left and right odom ports
- Disconnect laptop power and secure the cable away from tractor
- Clear everything away from the tractor
- Move the RC control to manual (middle) check steering and transmission control
- Put the RC control speed to neutral and steering to straight
- Disconnect the battery charger (i.e. shore power) if it is connected
Start Sequence
- Confirm pre-planning steps are complete (e.g. plan copied, IMU initial yaw set)
- Launch GUI; python3 ~/ros1_lawn_tractor_ws/project_notes/code_for_testing/gui/gui_main_v1.py
- Press “Start”
- Watch for any error messages.
- Wait for RTK status to be non-red and for Serial 1 and 2 to be green
- Confirm the IMU is working; $ rostopic echo /imu/data
- Start tractor engine
- Press “Location 2”
- Engage transmission
- Drive to starting position

Lawn Tractor Shutdown / Parking

At Tractor
- Open laptop, Press “Stop”
- Use RC control or Red button to stop motor
- Turn off master power
- Disengage transmission
- Connect laptop for charging if leaving it on
- Disconnect 12 volt power from USB hub
- Turn off battery BMS using BMS software
- Reconnect battery charger if needed

At Base Station
- Disconnect Power
- Store battery

For Radio Control
- Disconnect Power
- Store unit in a safe place

Note: For older version and comments see 2023 version

Field Testing Supplies
- Deep woods off
- Wasp spray
- Dress for the outdoors (Coat if cold; Ball cap if sunny)
- Power supply
- Tools
  - Plain and phillips screw driver
  - Sockets to disconnect lithium battery
- Battery for RC controller
- 12 Volt battery for base station