Test steering and throttle control

Manual control testing - goal is to establish PID settings, and confirm mode_sw = manual
Put power supply on to charge the battery
- Use battery BMS to engage power on the charge side using the slide switch
- Get power to the motor
  - Connect wires from steering motor to motor power supply
  - Connect wires from steer angle sensor to appropriate connector
- Put the mode switch on the radio control into the middle position “manual”
- Use battery BMS to engage power on the discharge side using the slide switch; The steering motor should be live now.
- Plug in 12V supply to the USB hub
- Engage master power red handle
- If PID is not established
  - Set all PID settings to zero (0)
  - Move the target steering slightly to the right
  - Slowly increase Kp until the steering motor engages and the wheels move
  - Adjust Kp to find the extremes
  - Reset the map function to be nearer to the extremes to fine tune Kp

cmd_vel control testing – goal is to confirm ability for tractor to steer from cmd_vel statements between -0.73 and 0.73

- Set mode switch to manual
- Confirm you have manual control of the steering
- Set model switch to cmd_vel

The manual way to publish cmd_vel is: $ rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.3, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.0}}'

rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.5}}'

Input into file: testing_cmd_vel_pub_input.txt
0.0, 0.0, 5 / 0.0, 0.25, 5 / 0.0, 0.5, 5 / 0.0, 0.0, 5 / 0.0, -0.25, 5 / 0.0, -0.5, 5
$ cd /home/tractor/ros1_lawn_tractor_ws/project_notes/code_for_testing / $ python3 testing_cmd_vel_pub.py

1. Test transmission, while disengaged, no motor running
  1. Manual control - mark the position of the control lever in order to check against cmd_vel statements
  2. Issue rostopic pub cmd_vel for forward (1.8), reverse (-1), neutral (0)
2. Motor running - on blocks
  1. Manual control
    1. What value starts to move wheels forward
    2. What value starts to move the wheels backward
    3. Does that match "73" as neutral?
3. Motor Running - In the yard
  1. Manual control - Use wheel odom data and the GPS data
  2. Adjust the transmissionFullForwardPos until speed achieves 1.8 m/s
  3. Adjust transmissionFullReversePos until -1.0 m/s is achieved when full reverse
4. Cmd_vel control
  1. Simple one position
  2. Simple 3 positions - straight line

OLD NOTES
Assumptions
- Motor is mounted, but not powered
- Angle sensor is mounted, connected to the Teensy which is connected to the RPi and basic testing has been conducted
- The sensor value for hard right and hard left is known

To be completed in this step:
- 3D print the holder for the motor controller and Teensy
- Connect 12V power to the motor controller from battery
- Connect the motor controller (GND, Direction and PWR level) to the Teensy
- Fasten the motor controller and Teensy to the motor mount

- Connect the motor controller power leads to the motor
- Run sample program that reads steering sensor
  - Connect USB drive
    - Make cable long enough to connect
    - Route cable
    - See which devices are currently connected $ ls /dev/ttyACM*
      - /dev/ttyACM0 /dev/ttyACM1 /dev/ttyACM2 /dev/ttyACM3
  - Create a UDEV rule for the front_angle Teensy

1. Create a UDEV rule for the front_angle Teensy
  1. Background: https://arduino.stackexchange.com/questions/3680/in-linux-how-to-identify-multiple-arduinos-connected-over-usb; http://www.googlinux.com/clearing-dmesg-logs/index.html
  2. Logon to the RPI; Confirm the teensy is able to be seen by RPi. $ ls /dev/ttyACM*, then connect front angle sensor, $ ls /dev/ttyACM*
  3. Unplug / turn off power to any USB devices
  4. Save the dmesg log. $ dmesg > dmesg-`date +%d%m%Y`.log
  5. Clear the log. $ sudo dmesg -c
  6. Plug in the Teensy to be used. Remember this has a unique serial number.
  7. List the dmesg $ dmesg
  8. Results:
ubuntu@ubiquityrobot:~$ dmesg / [118616.881363] usb 1-1.3.2: new full-speed USB device number 45 using dwc_otg / [118617.014192] usb 1-1.3.2: New USB device found, idVendor=16c0, idProduct=0483 / [118617.014207] usb 1-1.3.2: New USB device strings: Mfr=1, Product=2, SerialNumber=3 / [118617.014215] usb 1-1.3.2: Product: USB Serial / [118617.014223] usb 1-1.3.2: Manufacturer: Teensyduino / [118617.014230] usb 1-1.3.2: SerialNumber: 5588760 / [118617.015401] cdc_acm 1-1.3.2:1.0: ttyACM0: USB ACM device

- Setup udev rule mapped to “steer_motor ” because later you will want to update the setting: “upload port = /dev/steer_motor ” in the platformio.ini file. Background reading: https://linuxconfig.org/tutorial-on-how-to-write-basic-udev-rules-in-linux
- Edit and update this line, then copy it because it will be easier to paste into the editor.
- SUBSYSTEM=="tty", ATTRS{idVendor}=="16c0" , ATTRS{idProduct}=="0483" , ATTRS{serial}=="5588760", SYMLINK+="steer_motor"
- Change permissions so I can use FileZilla and Sublime to edit the udev files
  - $ sudo chmod -R 777 /etc/udev/rules.d/05-serial.rules
- $ sudo edit /etc/udev/rules.d/05-serial.rules
- Move the cursor to the end of the last character in the last line
- Press INSERT; Move the cursor to the end and press enter
- Copy the new line above and paste into the editor by right mouse clicking at the beginning of the new line.
- Press Escape to exit the insert mode
- Save the file by entering “:w” then enter
- Quit using “:q” then enter
- Reboot the RPi for the changes to take effect $ sudo reboot
- $ ls /dev/steer_motor to confirm the link has been made
Update PlatformIO environment ini
Open FileZilla, Update the platformio.ini file in /home/ubuntu; Add section for front_angle
; / [env:front_angle] / platform = teensy / board = teensy31 / framework = arduino / upload_port = /dev/front_angle

“board = teensy35” is used for a Teensy 3.5
1. Update bash scripts to help PlatformIO compiling
  1. Background: There are two bash scripts that have been used for compiling, compile_a.sh and compile_b.sh. These scripts need to be updated because you have a new microcontroller connected to the USB hub.
  2. Connect all the USB cables and run $ grep 16c0 /sys/bus/usb/devices/*/idVendor to list all the Teensy devices connected.
  3. For testing, run the scripts without the platformio or roslaunch commands enabled. I had issues getting permissions correct.
  4. If you reboot, to resolve permission issues run:
    1. $ sudo chown root:plugdev /sys/bus/usb/drivers/usb/{bind,unbind}
    2. $ sudo chmod g+w /sys/bus/usb/drivers/usb/{bind,unbind}
    3. See: https://community.platformio.org/t/multiple-boards-upload-port-works-but-crashes-2nd-board/9029/8

ubuntu@ubiquityrobot:~$ grep 16c0 /sys/bus/usb/devices/*/idVendor / /sys/bus/usb/devices/1-1.3.1.1/idVendor:16c0 (joystick) / /sys/bus/usb/devices/1-1.3.1.2/idVendor:16c0 (left speed) / /sys/bus/usb/devices/1-1.3.1.3/idVendor:16c0 (transmission) / /sys/bus/usb/devices/1-1.3.1.4/idVendor:16c0 (front_angle) / /sys/bus/usb/devices/1-1.3.2/idVendor:16c0 (steer_motor) / (NOTE: Put the latest device IDs in the file “Documenting the Teensy device ID’s”)

File: compile_a.sh / #!/bin/bash / # this script to "turn off" the USB ports and to start the compile process / # / # Comment out the device you will be programming / # / # (1 of 2) Comment OUT the device you WILL be programming or devices not connected / # / #echo -n "1-1.3.1.1" > /sys/bus/usb/drivers/usb/unbind # diy joystick / echo -n "1-1.3.1.2" > /sys/bus/usb/drivers/usb/unbind # left speed / echo -n "1-1.3.1.3" > /sys/bus/usb/drivers/usb/unbind # transmission / echo -n "1-1.3.1.4" > /sys/bus/usb/drivers/usb/unbind # front_angle / #echo -n "1-1.3.2" > /sys/bus/usb/drivers/usb/unbind # steer_motor / # / # (2 of 2) UN-COMMENT the line for the platformio environment you WANT TO COMPILE / # / # Platformio environments include: [env:joystick], [env:left_speed], [env:transmission], [env:front_angle], [env:steer_motor] / #sudo platformio run -t upload -e front_angle # for [env:front_angle] / sudo platformio run -t upload -e steer_motor # for [env:steer_motor] / #sudo platformio run -t upload -e transmission # for [env:transmission]

File: compile_b.sh / #!/bin/bash / # this script to "turn on" the USB ports after the compile process is complete / # / # Comment OUT the board that IS being programmed. It will not need the "bind" statement. All other connected devices should be active. / # / #echo -n "1-1.3.1.1" > /sys/bus/usb/drivers/usb/bind # joystick / echo -n "1-1.3.1.2" > /sys/bus/usb/drivers/usb/bind # left speed / echo -n "1-1.3.1.3" > /sys/bus/usb/drivers/usb/bind # transmission / echo -n "1-1.3.1.4" > /sys/bus/usb/drivers/usb/bind # front_angle / #echo -n "1-1.3.2" > /sys/bus/usb/drivers/usb/bind # steer_motor / # / # start the launch file that will initiate the Teensy's you want to test / cd /home/ubuntu/catkin_ws/src / roslaunch teensy_launch.launch / #roslaunch steer_test_launch.launch / #roslaunch transmission_test_launch.launch

To test:
- $ grep 16c0 /sys/bus/usb/devices/*/idVendor
- $ ls /dev/ttyACM*
- If you have code to compile and multiple Teensy’s are connected and active, run $ bash compile_a.sh then $ ls /dev/ttyACM*
- Alternatively if the USB ports are still unbound (i.e. only one Teensy active), run $ sudo platformio run -t upload -e steer_motor
- Once compile is clean and you want to test, run $ bash compile_b.sh then $ ls /dev/ttyACM*
- If you have seen how they appear, disappear and reappear, you can now take out the comment for the PlatformIO statement in compile_a.sh
  1. If USB ports are still unbound, run $ sudo platformio run -t upload -e steer_motor
1. Test compiling and running blink.cpp
2. Update launch file - steer_test_launch.launch to only launch the angle and motor controller teensy.

steer_test_launch.launch
<launch> / <?ignore - used to comment out lines / <node ns="transmission_teensy" name="transmission_cntrl" pkg="rosserial_python" type="serial_node.py" args="/dev/transmission_control" output="screen" /> / <node ns="potentiometer_teensy" name="potentiometer_output" pkg="rosserial_python" type="serial_node.py" args="/dev/potentiometer_control" output="screen" /> / <node ns="left_speed_teensy" name="left_speed" pkg="rosserial_python" type="serial_node.py" args="/dev/odom_left" output="screen" /> / ?> / <node ns="front_angle_teensy" name="front_angle" pkg="rosserial_python" type="serial_node.py" args="/dev/front_angle" output="screen" /> / <node ns="steer_motor_teensy" name="steer_motor" pkg="rosserial_python" type="serial_node.py" args="/dev/steer_motor" output="screen" /> / </launch>

1. Test program
  1. Once you have a complete compile and before launching the programs
    1. Check power to motor
    2. Ensure the work area is clear; Double check the steering rods and there are no obstacles (e.g. wires) in the way
    3. Remind yourself where to disconnect power should you need to do so
    4. On RPi,
      1. $ ls /dev # you should only see one teensy (i.e. steer_motor)
      2. Run $ bash compile_b.sh
      3. Optionally if the bind statements have already been run:
        1. $ cd /home/ubuntu/catkin_ws/src
        2. $ roslaunch steer_test_launch.launch
  2. On Laptop
    1. Ctrl+Alt+T, $ rqt
    2. Organize rqt screens to monitor steering PWM, cmd_vel/angular/x and front_angle_klm/data. Use “dock” icon to move screens to desired position

    1. Connecting the joystick - See Step 4 - Install ROS-Ag lawn tractor simulator section Test drive using gamepad for background and to confirm port identifier.
    2. Start joy_input to transfer data to cmd_vel:
- Ctrl+Alt+T, $ roslaunch tractor_teleop cmd_vel_mux.launch
- Ctrl+Alt+T, $ roslaunch tractor_teleop drive_teleop.launch joy_dev:=/dev/input/js0
- Note: drive_teleop.launch has as a default: <arg name="joy_dev" default="/dev/input/js0"/> If your joystick is on js1 you can either change the launch file or adjust the argument.
- Alternatively, the command below has both of the above commands combined
  - $ roslaunch tractor_teleop drive.launch
    - At this point you should be able to press the deadman switch, move the steering joystick and see the target angular.z adjust.

Next Step
Confirm steer straight and left right settings.

Choose Plugins -> Robot Tools -> Robot Steering

In the rqt topic put /teleop/cmd_vel in the topic field

On the RPi echo the topic and move the slider in rqt to see the topic being published

Drag the window all the way to the right
- You can now adjust the slide bars and send cmd_vel command using this interface
- An alternative is to run a bash script written for this purpose.
#!/bin/bash / timeout 10 rostopic pub -r 10 teleop/cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.5}}' / timeout 10 rostopic pub -r 10 teleop/cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.0}}' / timeout 10 rostopic pub -r 10 teleop/cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.5}}'

Plugins -> Visualizations -> Plot will allow you to subscribe and visualize (i.e. plot) rostopics
Plugins -> Topics -> Topic Monitor lets you drag and drop the topics you are interested in

Testing protocol

Cmv_vel angular.z	Points to look for
0.0	Is the steering steady and straight; Is the steer effort zero
0.03 to -0.03	Does the steering react and move to these smaller increments
Move from 0 to +/- .5	Does the steering reach the target and steer effort go to zero? What there overshoot? How long did it take to achieve the target?
1 and -1	Does the steering reach the target and steer effort go to zero? What there overshoot? How long did it take to achieve the target?

Example output going from: 0.0 -> -0.5 -> +0.5 -> -0.7 -> +0.7 -> 0.0

$ timeout 3 rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.5}}'
$ timeout 3 rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.75, y: 100.0, z: 0.0}, angular: {x: 200.0,y: 0.0,z: 0.0}}'

10/15/19

Using rosparam to change settings
The command <rosparam param="steering">[28900.1, 46300.0, 36500.0, 50.0, 2.0]</rosparam> is located in the teensy_launch.launch and steer_test.launch files. This sets the steering parameters:
steer_left_max = 28900;
steer_right_max = 46300;
steer_straight = 36500;
max_steer_eff = 50;
steer_Ki = 2;

The command that will also do the same thing is $ rosparam set /steering "[28900.0, 46300.0, 36500.0, 50.0, 2.0]"

 I adjusted the steer straight to be 36800
10/18/19
$ rosparam set /steering "[28900.0, 46300.0, 38000.0, 70.0, 2.0]"

Once you have the transmission running you can further tune the settings. For example, in the grass, get the steer_effort adjusted

3/1/20
Import KLM perspectives in rqt
Dragging from right to left with the right mouse button down will slow down the speed of the plot.
Press the up/down arrow pan axis first
Doing the same up and down to zoom in on the preferred range.

Straight ahead / position_klm: 36102
Full left / position_klm: 27184 / Full right / position_klm: 47415

The steering is not making the full rotation; Check variables being passed.

5/17/20
$ timeout 3 rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.5}}'
No movement at all - This issue was the signal wire to the motor controller had come loose.
$ rosparam set /steering “[27900.0, 45798.0, 36874.0, 60.0, 3.0]”

- $ rosparam set /steering "[27900.0, 45798.0, 36874.0, 60.0, 3.0]"
- $ rosparam set /steering "[23600.0, 44300.0, 33319.0, 60.0, 3.0]"
<rosparam param="steering">[24300.0, 44000.0, 34000.0, 70.0, 3.0]</rosparam>

5/18/20
The wheels banged into a big ant mound and turned the wheels hard one direction. I need to re-confirm left, right, center.

Current:$ rosparam get /steering
[24300.0, 44000.0, 34000.0, 70.0, 3.0]

Left

Right

$ rosparam set /steering "[27400.0, 45200.0, 35600.0, 70.0, 3.0]"

0.5, -0.3, 60 - produces a circle about 15’ in diameter
0.5, -0.2, 60 - produces a circle about 17’ in diameter

Positive still produced a right hand turn!

0.5, 0.005, 60

After 30 minutes of testing the center seems to be off which is leading to the inability to turn left.

I need to recenter.: 29209

Full left: 19200
Full right: 42000
42022

$ rosparam set /steering "[19200.0, 42000.0, 29209.0, 70.0, 3.0]"

Pulling left when going straight

- rosparam set /steering "[19200.0, 42000.0, 30000.0, 70.0, 3.0]"
- rosparam set /steering "[19200.0, 42000.0, 30400.0, 70.0, 3.0]"

Center has become unadjusted again. It is near 40000!

Just to get the tractor back
rosparam set /steering "[38200.0, 46000.0, 42000.0, 70.0, 3.0]"

5/22/20
2 rotation potentiometer keeping track of the rotations

Continuous rotation potentiometer
https://www.usdigital.com/products/encoders/absolute/magnetic/MA3